## Slide 1: Tutorial for ambient noise tomography processing using SeisImager/SW-3D
Processing ambient noise data obtained by Atom.
SeisImager/SW-3D license is required.
Download the latest installer from : https://seisimager.com/download/SeisImager.zip
Download the example data from : http://seisimager.com/download/mam_2d.zip
See “2D/3D ambient noise tomography processing using SPACPlus and other SeisImager modules” for more details

## Slide 2: Data acquisition
55 m (5 m spacing)
After 10 min.
After 10 min.
100007
100042
100049
100048
100047
100050
100054
100070
100071
100072
100073
100074
100007
100042
100048
100047
100049
100050
100054
100070
100071
100072
100073
100074
100049
100050
100054
100070
100007
100042
100048
100047
100071
100072
100073
100074

## Slide 3: Import Atom data files
Double click icon to launch SPACPlus
Select “File”, “Open folder”.
Select a root folder of data.

## Slide 4: Import Atom data files
Confirm number of seismograph (Atom acquisition units).
Confirm number common time blocks (CTB).

## Slide 5: Common time blocks (CTBs)
The example data include 20 CTBs.
CTB 0
CTB 1
CTB 19

## Slide 6: Prepare geometry file (MAM 2D Geometry.txt)
.
.
CTB index
Atom ID
X
Y
0 100007 0 0
0 100042 5 0
0 100047 10 0
0 100048 15 0
0 100049 20 0
0 100050 25 0
0 100054 30 0
0 100070 35 0
0 100071 40 0
0 100072 45 0
0 100073 50 0
0 100074 55 0
1 100049 20 0
1 100050 25 0
1 100054 30 0
1 100070 35 0
1 100071 40 0
1 100072 45 0
1 100073 50 0
1 100074 55 0
1 100007 60 0
1 100042 65 0
1 100047 70 0
1 100048 75 0
2 100071 40 0
2 100072 45 0
2 100073 50 0
CTB 0
CTB 1
CTB 19
17 100049 380 0
17 100050 385 0
17 100054 390 0
17 100070 395 0
18 100007 360 0
18 100042 365 0
18 100047 370 0
18 100048 375 0
18 100049 380 0
18 100050 385 0
18 100054 390 0
18 100070 395 0
18 100071 400 0
18 100072 405 0
18 100073 410 0
18 100074 415 0
19 100049 380 0
19 100050 385 0
19 100054 390 0
19 100070 395 0
19 100071 400 0
19 100072 405 0
19 100073 410 0
19 100074 415 0
19 100007 420 0
19 100042 425 0
19 100047 430 0
19 100048 435 0

## Slide 7: Import geometry file
Select “2D/3D”, “Open sensor location file” Open sensor location file.
Select geometry file.
Confirm number of sensor locations.

## Slide 8: Show geometry
Select “2D/3D”, “Show geometry” to show geometry or sensor locations etc.
Sensor location, geometry, and/or receiver pairs appear. Use “View” menu to switch/select elements to be shown.

## Slide 9: Set up bin size of CMP grids
Select “2D/3D”, “Set bin size” to set up bin (grid) size.
Set bin (grid) size and are of processing if necessary.
CMP grids do not appear in the case of 2D.

## Slide 10: Calculate CMP-SPACs
Select “2D/3D”, “CMP SPAC”.
Set (confirm) Bin size and click “OK” to start calculation.
Confirm number of CTBS etc.

## Slide 11: Calculate CMP-SPACs
Several messages appear and confirm them.
Calculation will take several minutes.
After completing CMP-SPAC calculation, Pickwin shows CMPSPACs. Click “Yes” to continue.

## Slide 12: Show CMP-SPACs by Pickwin
Pickwin is automatically launched and a file list of CMP-SPACs appear.
Click “OK” to continue.

## Slide 13: Show CMP-SPACs by Pickwin
SPAC (coherence) appears. Use buttons to scroll the bins (SPAC files).

## Slide 14: Calculate dispersion curves
Select “Surface wave analysis”, “Phase velocity-frequency transformation and picking (2D/3D)”.
Set phase velocity and frequency ranges.

## Slide 15: Calculate dispersion curves
Set minimum frequency and necessary parameters.
Click “Advanced menu” to set up detailed parameters.
It will take a while to complete the calculation.

## Slide 16: Show dispersion curves by WaveEq
Select “Surface wave analysis”, “Show Phase velocity curves (2D/3D)”.
WaveEq is automatically launched and phase velocity curves appears.

## Slide 17: Show dispersion curves by WaveEq
Use to scroll dispersion curves.
Use to change how many dispersion curves are shown.
Delete noises or unnecessary phase velocities like 1D/2D processing.

## Slide 18: Create an initial velocity model
Select “MASW (2D/3D)”, “Initial model”.
Set depth and the number of layers of model.

## Slide 19: Create an initial velocity model
Initial velocity model appears.
Use to change how many velocity profiles are shown like dispersion curves.

## Slide 20: Show 2D velocity model by GeoPlot
Select “MASW (2D/3D)”, “Show 2D velocity model <launches GeoPlot>”. Note that you can apply inversion before showing 2D velocity model.
GeoPlot is automatically launched.
See “GeoPlotTM Manual” for more details about GeoPlot

## Slide 21: Apply inversion
Select “MASW (2D/3D)”, “Inversion (2D/3D:All data)” to apply inversion to all dispersion curves at once.
See “SeisImager/SW-ProTM Manual” for more details about various inversion.
Set the number of iteration for inversion and click “OK” to start the inversion.